## Slide 1
Classification of the Motor Imagery
2017.6.14
In-Nae Wang
Hyung-Joon Moon
Yong-Jeong Kim
Pattern Recognition and Machine Learning TERM PROJECT

## Slide 2
I. Introduction
Introduction
Goal
  Classifying the 2-Class Motor Imagery (MI) through various methods
  CSP-LDA, CNN, Logistic Regression
Background
  Motor Imagery
  Mental process by which an individual rehearses or simulates a given action
OR
…
Ch 1
Ch 2
Ch N
…
Signal processing

## Slide 3
I. Introduction
Dataset : from BCI Competition III
BCI competition III_4a
  5 subjects who performed right-hand and foot imagination
  280 trials of EEG measurements from 118 electrodes
  Selected 19 channels
    Motor area: 19 channels (FC5, FC3, FC1 Etc)
  Segmentation which is starting from 0.5s to 3.5s after the visual cue
  10×10-fold cross-validation
Motor Imagery recording procedure
EEG channels used in classification

## Slide 4
II. Methods & Results
Our Approaches for Classification
LDA
1D Conv-Net
2D Conv-Net with Spectrogram
Logistic Regression

## Slide 5
1. LDA
Standard way to analyze EEG data
II. Methods & Results
Band-Pass Filter (BPF): 8~30 Hz
Common Spatial Pattern (CSP)
  Maximizing the ratio for covariance of two tasks
Linear Discriminant Analysis (LDA)
  Maximizing the between-covariance Minimizing the within-covariance
BPF: 8~30 Hz
(Preprocessing)
LDA (Classification)
EEG Raw Signals
CSP -> logvar
(Feature Extraction)

## Slide 6
III. Results
1. LDA (Results)
Avg. 88% classification performance
Showed High Energy around 10Hz
Time-freq. representation for right-hand motor imagery
Subject | Right Hand vs Foot
aa | 0.82
al | 0.97
av | 0.72
aw | 0.95
ay | 0.95
Avg. | 0.88
The classification results of LDA

## Slide 7
III. Results
1. LDA (Reference)
Analysis of the spatial filter & pattern
Filter
Pattern
Pattern
Filter
Right
Foot
Subject: 3
Subject: 5

## Slide 8
III. Results
2. 1D Conv Net
Our Architecture Over view
time
280 trial
19 Channel
EEG Data
Array Structure

## Slide 9
III. Results
2. 1D Conv Net
For Deeper Conv Net in Small DATA, We Tried,
  Parameter dimension control : 15k ~ 30k
  1 x 1 layer to reduction of features
  Kernel initializer : He-Uniform
  Activation : Leaky Relu
So…deep. Will this work?

## Slide 10
III. Results
2. 1D Conv Net (Results)
In very Deep
Early Stop
Early Stop
In Not so Deep

## Slide 11
III. Results
2. 1D Conv Net (Results – 10fold cross valid.)
It worked quite well, but not not satisfied. (failed in subj 3)
Subject | Right Hand vs Foot
aa | 0.86
al | 0.95
av | -
aw | 0.95
ay | 0.90
Avg. | 0.91 (?)
The classification results of 1D Conv
Confusion Matrix for one sample test-set

## Slide 12
III. Results
3. Logistic regression
Logistic regression
Statistical techniques used to predict the likelihood of an event using linear combination of independent variables(EEG raw data).
By finding the relationship between the independent variable (𝑋) and the dependent variable (𝑌), we can predict the dependent variable (𝑌) when given a new set of independent variables().
Since the dependent variable is categorical data and when the input data is given, the result of the data is classified into a specific classification.

## Slide 13
III. Results
3. Logistic regression
Learning method: Logistic regression finds the optimal β for the independent variable x satisfying
ε corresponds to the standard logistic distribution. The predicted value is defined by
All real numbers can be input, and the output is easy to judge the result by taking a probability value between 0 and 1.

## Slide 14: Thank you