## Slide 1: Pattern Recognition for Interpretable BCI
2017.06.14
Geun-Ho Choi O-Yeon Kwon

## Slide 2: Contents
1. Introduction
  Goal
  Concept of Brain Computer Interface (BCI)
2. Methods
  1. Conventional framework
  2. Deep learning framework
3. Results and discussion
4. Conclusion

## Slide 3: Introduction
Goal
  Use pattern recognition methods and build extensive knowledge in the field of pattern recognition
  Obtain a high classification accuracy in the filed of Brain computer inter face (BCI) by using a novel method
Motivation
  Focusing on the recognition of patterns and regularities for the interpretation of data
BCI classification pipeline [Samek, 2014]

## Slide 4: Brain Computer Interface (BCI) (1/2)
Definition
  BCI is a direct communication pathway between an enhanced or wired brain and an external device [Wikipedia]
Application
  Focusing on neuroprosthetics applications that aim at restoring damaged hearing, sight and movement
  Brain computer interfaces have been used for a much broader variety of applications
Neuroprosthetics
Applications

## Slide 5: Brain Computer Interface (2/2)
Electroencephalography (EEG)
  An electrophysiological monitoring method to record electrical activity of the brain - Wikipedia
Motor Imagery (MI)
  A mental process by which an individual rehearses or simulates a given action – Wikipedia
    e.g., left hand or right hand movement imagination
Different approaches of BCI
EEG measurement and MI task
Motor Imagery
SSVEP
P300
Thought Control [Nature, 2012]

## Slide 6: Methods (1/3)
Dataset
  Description
    BBCI_IV Data Set 2b
      9 subjects (C3, Cz, C4 channels)
Paradigm
  Motor Imagery
    Subjects were instructed with a text on the monitor to perform either up-down or left-right movements
Data analysis
  1. Pre-processing
    Band-pass-filter (8-30 Hz)
    Segmentation (4s - 7s)
  2. Feature extraction
    1. Log-variance
    2. Common Spatial Pattern (CSP)
  3. Classification
    Linear Discriminant Analysis (LDA)
  4. Evaluation
    10-fold-cross validation with 10 iterations
      2 classes - (360 training / 40 test)
Description of BBCI dataset

## Slide 7: Methods (2/3)
Common Spatial Pattern (CSP)
  Mathematical procedure used in signal processing for separating a multivariate signal into additive subcomponents which have maximum differences in variance between two windows
Geometrical interpretation of the optimization CSP framework [Samek, 2014]

## Slide 8: Methods (3/3)
Linear Discriminant Analysis (LDA)
  A method used in statistics, pattern recognition and machine learning. to find a linear combination of features that characterizes or separates two or more classes of objects or events
Two-dimensional example of a binary classification setting [S. Haufe et al., 2014]

## Slide 9: Results
 | Log-var / LDA (10 fold) / 10 iter |  |  | C3/Cz/C4
 | 7-13Hz | 8-30Hz | 1-100Hz | 
1 | 0.72 | 0.69 | 0.63 | 
2 | 0.59 | 0.61 | 0.57 | 
3 | 0.56 | 0.55 | 0.54 | 
4 | 0.89 | 0.89 | 0.85 | 
5 | 0.66 | 0.75 | 0.63 | 
6 | 0.67 | 0.72 | 0.61 | 
7 | 0.60 | 0.67 | 0.59 | 
8 | 0.69 | 0.69 | 0.67 | 
9 | 0.70 | 0.73 | 0.70 | 
Mean | 0.68 | 0.70 | 0.64 | 
 | CSP / LDA (10 fold) / 10 iter |  |  | C3/Cz/C4
 | 7-13Hz | 8-30Hz | 1-100Hz | 
1 | 0.75 | 0.73 | 0.65 | 
2 | 0.59 | 0.58 | 0.58 | 
3 | 0.54 | 0.52 | 0.54 | 
4 | 0.89 | 0.89 | 0.85 | 
5 | 0.68 | 0.74 | 0.68 | 
6 | 0.68 | 0.71 | 0.61 | 
7 | 0.67 | 0.73 | 0.58 | 
8 | 0.72 | 0.68 | 0.67 | 
9 | 0.71 | 0.76 | 0.72 | 
Mean | 0.69 | 0.70 | 0.65 | 
1. Log-variance features and LDA
  It showed a 70% average accuracy
    Subject 4 showed a good result, but subject 3 had a bad result
    It showed different average accuracies with different frequency information
2. CSP features and LDA
  It showed a 70% average accuracy
    It showed a similar result with above result for each person
    It indicated the CSP features and log variance features are giving similar results in this dataset
Log-variance feature accuracy based on LDA
CSP feature accuracy based on LDA

## Slide 10: Discussion
Subject 4
Subject 3
Log-variance - LDA
CSP - LDA
1. Feature distribution
  Intuitively, subject 4 showed a well-distributed distribution for classification
  But, subject 3 showed a not suitable distribution for classification
2. Log-variance vs CSP
  It does not look like a huge difference between them
Feature distribution of data samples

## Slide 11: Deep learning in BCI
Related works
  In the BCI literature, Deep learning is being used little by little in nowadays
  According to [Y.R. Tabar, 2017], they show high performance MI task using deep learning method
[Y.R. Tabar, 2017]

## Slide 12: Proposed Model
Input : time domain BCI dataset (without FFT)
  [Y.R. Tabar, 2017] uses Short Time Fourier Transform (STFT)
  Our method is more simple without loss of accuracy
Model : 7 Convolutional layer
  With Batch-normalization, max-pooling (1x2)
Cov1
Cov2
Cov3
Cov4
Cov5
Cov6
Cov7
FC
Proposed model
Conv1
Conv2
Example of layers
Raw input

## Slide 13: Results
Ablation study
  1 layer : decreasing accuracy of 2%
  BatchNorm : increasing training speed
It showed a 74% average accuracy among subjects
  It showed a similar results compared to the conventional method (aforementioned results)
  Our model’s accuracy is similar to accuracy of CNN with STFT of [Y.R. Tabar, 2017]
 | CNN 7 layer / 10 iter |  |  | C3/Cz/C4
Subjects | 7-13Hz | 8-30Hz | 1-100Hz | 
1 | 0.75 | 0.70 | 0.65 | 
2 | 0.52 | 0.56 | 0.45 | 
3 | 0.50 | 0.47 | 0.50 | 
4 | 0.95 | 0.95 | 0.95 | 
5 | 0.73 | 0.83 | 0.82 | 
6 | 0.62 | 0.65 | 0.60 | 
7 | 0.73 | 0.80 | 0.80 | 
8 | 0.85 | 0.78 | 0.88 | 
9 | 0.83 | 0.87 | 0.85 | 
Average | 0.72 | 0.74 | 0.72 | 
CNN model accuracy
[Y.R. Tabar, 2017]
Our model

## Slide 14: Discussion
To interpret the BCI classification results, we use two CNN layer visualization methods
1. Class Model Visualisation (a.k.a. saliency)
  Deep Inside Convolutional Networks: Visualising Image Classification Models and Saliency Maps [K. Simonyan, 2014]
2. Class Activation Map
  Learning Deep Features for Discriminative Localization [B. Zhou 2015]

## Slide 15: Visualization – Class Model Visualisation
Deep Inside Convolutional Networks: Visualising Image Classification Models and Saliency Maps [K. Simonyan, 2014]
  λ is the regularization parameter
  A locally-optimal I can be found by the back-propagation method
  The optimization is performed with respect to the input image (), while the weights are fixed to those found during the training stage
  Initializing the optimization with the zero image

## Slide 16: Visualization – Class Model Visualisation (Cont’d)
Ideally, left class pattern shows that C4 pattern is higher than C3 and vice versa
Showing that 3 channels are coupled together
  Further research is needed to ensure that the model decouples 3 channels
Combination of left, right classes pattern graphs
Right class pattern
Left class pattern

## Slide 17: Visualization – Class Activation Map
  Learning Deep Features for Discriminative Localization [B. Zhou 2015]
for a given class c, the input to the softmax, Sc, is
  where is the weight corresponding to class c for unit k
  =
  is the class activation map for class c

## Slide 18: Visualization – Class Activation Map (Cont’d)
Comparison between person 4(accuracy=0.95) and person 3(accuracy=0.5)
  person 3(accuracy=0.5) shows complex and multi-modal graph
  person 4(accuracy=0.95) shows simple and unimodal graph
person 3 – CAM (left class)
person 3 – raw input (left class)
person 3 – raw input (right class)
person 3 – CAM (right class)
person 4 – CAM (left class)
person 4 – raw input (left class)
person 4 – raw input (right class)
person 4 – CAM (right class)

## Slide 19: Visualization – Class Activation Map (Cont’d)
Comparing Class Activation Map with Time-amplitude topoplot
  At the 2/3 area of CAM (right class) C3 activation value is sharply increased
  At the 6th topoplot C3 activation value is sharply increased
  We can conjecture that our model classify in terms of which channel shows high amplitude
Time-amplitude topoplot for subject 4 (trial 127)
person 4 (trial 127) – CAM (right class)
person 4 (trial 127) – CAM (left class)

## Slide 20: Conclusion
Results
  Conventional way : accuracy is 70%
  Deep learning way : accuracy is 74%
Contribution
  Comparing conventional method and deep learning method
  Identifying our model’s drawback through CNN visualization method
  Trying to explain deep learning model in the BCI process, which is not fully covered yet in the BCI literature
  We can research further thanks to this project